## Slide 1: At 80 ktpa, KBR CAPEX is $413M; Air Liquide's implied CAPEX is 1.44× higher
Chart: MM USD
| KBR H2ACT® | Air Liquide (implied from fee)
ISBL | 208 | 0
OSBL | 71.6 | 0
Other CAPEX | 133.1 | 0
Air Liquide implied CAPEX | 0 | 595.601
Total | 412.7 | 595.601
$413M
ISBL 208 + OSBL 72 + other CAPEX 133
$596M
Air Liquide implied CAPEX, from the yearly tolling fee
1.44×
Air Liquide ÷ KBR, a gap of $183M
Basis: 80 ktpa H₂, 350 stream days, natural gas main fuel 6.5 t NH₃/t H₂; NH₃ 687 USD/t, power 140 USD/MWh, gas 13 USD/MMBtu. Other CAPEX = start-up, spares, catalyst, licence, owner's costs 7.5 %, contingency 25 %, escalation 3 %/yr × 2 yr. KBR is Class V (±50 %) and excludes Terminal & Storage, land, taxes and IDC. Air Liquide is implied from a yearly tolling fee that includes operator return, a different basis; indicative only.
Notes: KBR CAPEX = ISBL (power-law fit to KBR §4.1) + OSBL (KBR total derived from its LCOH, minus ISBL) + other CAPEX (Gentari assumptions). Air Liquide = (yearly fee − licence) ÷ (CRF 9 %/20 yr + 3 % O&M), converted at 1.1448 USD/EUR. Chart data can be edited via Edit Data.

## Slide 2: Each added ktpa costs less at scale: KBR falls from $3.07M to $1.98M per ktpa between steps
Chart: H₂ capacity, ktpa
| 12 | 16 | 20 | 24 | 28 | 32 | 36 | 36.7 | 40 | 44 | 48 | 52 | 56 | 60 | 64 | 68 | 72 | 76 | 80 | 84 | 88 | 92 | 96 | 100 | 104 | 108 | 110 | 112 | 116 | 120 | 124 | 128 | 132 | 136 | 140 | 144 | 148 | 152 | 156 | 160 | 164 | 168 | 172 | 176 | 180
KBR, within source data (12–80 ktpa) | 179.4 | 202.5 | 222.7 | 241 | 257.4 | 272.8 | 287.2 | 289.72 | 301.6 | 314.24 | 326.88 | 338.94 | 350.42 | 361.9 | 372.42 | 382.94 | 393.1 | 402.9 | 412.7
KBR, extrapolated | 412.7 | 421.94 | 431.18 | 440.18 | 448.94 | 457.7 | 466.02 | 474.34 | 478.5 | 482.48 | 490.44 | 498.4 | 506.08 | 513.76 | 521.28 | 528.64 | 536 | 543.16 | 550.32 | 557.34 | 564.22 | 571.1 | 577.82 | 584.54 | 591.16 | 597.68 | 604.2
Air Liquide, within fee points (36.7–110 ktpa) | 435.519 | 450.88 | 468.508 | 485.192 | 501.057 | 516.199 | 530.701 | 544.628 | 558.037 | 570.976 | 583.486 | 595.601 | 607.355 | 618.772 | 629.878 | 640.693 | 651.238 | 661.528 | 671.579 | 676.52
Air Liquide, extrapolated | 277.371 | 311.575 | 340.959 | 366.994 | 390.535 | 412.13 | 432.155 | 435.519
Air Liquide, extrapolated (above 110) | 676.52 | 681.406 | 691.02 | 700.434 | 709.658 | 718.701 | 727.573 | 736.282 | 744.835 | 753.24 | 761.502 | 769.629 | 777.625 | 785.496 | 793.247 | 800.882 | 808.407 | 815.824 | 823.138
KBR at 24 / 80 / 160 ktpa | 241 | 412.7 | 571.1
Air Liquide at 24 / 80 / 160 ktpa | 366.994 | 595.601 | 785.496
Step change, MM USD (per added ktpa)
Step | KBR | Air Liquide
24 → 80 ktpa | +172 (3.07/ktpa) | +229 (4.08/ktpa)
80 → 160 ktpa | +158 (1.98/ktpa) | +190 (2.37/ktpa)
CAPEX level, MM USD
ktpa | KBR | AL | AL − KBR
24 | 241 | 367 | +126
80 | 413 | 596 | +183
160 | 571 | 785 | +214
Basis as on the previous slide. KBR: ISBL + OSBL + other CAPEX, published for 12–80 ktpa; 160 ktpa is extrapolated and KBR gives no train-split rule. Air Liquide: fee power law through €53.4M at 36.7 ktpa and €83.4M at 110 ktpa; 24 and 160 ktpa are outside that range. Per ktpa = step change ÷ added capacity.
Notes: Curve data is on the chart's Edit Data sheet. KBR points are sampled from the cracker model at 4 ktpa steps; Air Liquide is the fee power law.

## Slide 3: Scale cuts KBR specific CAPEX 2.8× from 24 to 160 ktpa; Air Liquide stays 1.38–1.52× KBR
Total CAPEX, MM USD
Chart: 
| 24 ktpa KBR | 24 ktpa AL* | 80 ktpa KBR | 80 ktpa AL | 160 ktpa KBR* | 160 ktpa AL*
KBR ISBL | 111.2 | 0 | 208 | 0 | 298.5 | 0
KBR OSBL | 52.4 | 0 | 71.6 | 0 | 85.7 | 0
KBR other CAPEX | 77.4 | 0 | 133.1 | 0 | 186.9 | 0
Air Liquide implied CAPEX | 0 | 366.994 | 0 | 595.601 | 0 | 785.496
Total | 241 | 366.994 | 412.7 | 595.601 | 571.1 | 785.496
Specific CAPEX, USD per t/yr of H₂
Chart: 
| 24 ktpa | 80 ktpa | 160 ktpa
KBR | 10042 | 5159 | 3569
Air Liquide | 15291 | 7445 | 4909
* Extrapolated beyond source data: KBR publishes 12–80 ktpa; the Air Liquide fee points span 36.7–110 ktpa. Same basis as slide 1. Air Liquide: (fee − licence) ÷ (CRF 9 %, 20 yr + 3 % O&M); the fee includes operator return, a different basis from KBR.
Notes: Totals above the stacked bars are a hidden-line series ('Total') so the chart stays fully editable. Edit the numbers via Edit Data.

## Slide 4: Basis and assumptions behind the numbers
KBR H2ACT®
ISBL: power-law fit to KBR's stated points, 78 / 110 / 191 / 209 MM USD at 12 / 24 / 68 / 80 ktpa
OSBL: KBR total installed (derived from its LCOH) minus ISBL, fitted on its own
Other CAPEX: start-up, spares, inventory, catalyst fill at 30 USD/kg, licence €2.7M, owner's 7.5 %, contingency 25 %, escalation 3 %/yr × 2 yr
Class V (±50 %); excludes Terminal & Storage, land, taxes, IDC
160 ktpa is extrapolated past KBR's 80 ktpa case
Air Liquide (Le Havre)
Yearly tolling fee: €53.4M at 36.7 ktpa, €83.4M at 110 ktpa; power law between them
CAPEX = (fee − licence €8.50/t H₂) ÷ (CRF + fixed O&M); 9 % real pre-tax, 20 years, O&M 3 %; 1.1448 USD/EUR
NH₃:H₂ 6.8 t/t, the midpoint of VTTI's 6.3–7.3 range (feed only, no CAPEX effect)
Fee includes operator return; scope, term and indexation are not stated
24 and 160 ktpa are outside the quoted fee range
Notes: Source: nh3-cracker-design.html model and docs/cracker-model-notes.md in the repository.